Using A PUB card to Update Pinball 2000™

The PUB (Prism Update Board) card is used to install a software update into a Pinball 2000™ machine. This is an alternative method to update a Pinball 2000™ machine without using a portable computer. The PUB card contains an update for both the Game Program and the Sound Program for a Pinball 2000™ machine. The game and version number is indicated on a label on the PUB card. The PUB card may be used to update any number of machines since it transfers its program to the FLASH memory in the Pinball 2000™ machine. The PUB card is also reusable. You may program other updates for any Pinball 2000™ machine into a PUB card using any computer that runs Windows ’95 and has a standard ISA expansion slot.

Using a PUB card to update a Pinball 2000™ Machine

To transfer a Pinball 2000™ update from a PUB card to your machine, follow these simple steps:

1. Turn off the power to the machine.
2. Use Backbox key to remove the backglass.
3. Slide the Logic all the way forward and let it pivot downward.
4. Remove the Logic Box Cover.
5. Make sure the jumper on the PUB card has been removed or is only on 1 of the 2 jumper pins.
6. Insert the PUB card in the open ISA slot in the logic box. The components on the card (on the same side as the written text) should face the rear of the machine.
7. Turn power on. The screen will show the progress of the 2-minute process.
8. Turn power off when indicated on the screen.
9. Remove the card by using the top edge as a handle.
10. Replace Logic Box Cover and secure the Logic Box and Backglass.
11. Turn power on to operate your updated machine.

Installing a new update into a PUB card

The PUB card stores the program update in reprogrammable FLASH memory. This allows you to transfer any update for any Pinball 2000™ machine into a PUB card. To do this you must have a computer running Windows ’95 with at least 1 available ISA expansion slot.

You will need to obtain the Pinball 2000™ “PUB card manager” program along with a Pinball 2000™ update file. These files as well as instructions for updating will be available for download at our pinball.com web site at the following address:

http://www.pinball.wms.com/tech/pin2000/